## Slide 1
Digital Image Processing | Sir Rana Adeel
AI-Based Image
Restoration
Web Application
GROUP MEMBERS
Husnain Faisal (23-ST-042)
Zeeshan Atif (23-ST-002)
Rayyan Idrees (23-ST-045)
Faseeh ul Hassan (23-ST-019)
April 2026
React 19
Python Flask
OpenCV
PyTorch
DnCNN
Full-Stack AI Application

## Slide 2
Project Overview
What we built and why it matters
Problem
Degraded images from noise, blur & low resolution are everywhere — but no unified web tool existed for multi-technique restoration.
Solution
A full-stack web app combining classical CV algorithms + DnCNN deep learning into one intuitive interface with live before/after comparison.
Impact
Users can restore photos instantly via browser — no install needed. Supports PNG, JPG, BMP, TIFF, WebP up to 16 MB.
3
Restoration Modes
17
DnCNN Layers
5
Image Formats
3
Tech Layers

## Slide 3
System Architecture
Three-tier client-server design
FRONTEND
React 19 + Vite
Upload • Comparison Slider • Results Display
▼
BACKEND API
Python Flask + CORS
REST Endpoints • File Handling • Request Routing
▼
PROCESSING
OpenCV + PyTorch
Denoise • Deblur • Super Resolution • DnCNN
Vite dev server proxies /api → Flask :5000 | Flask imports processing module directly as Python package

## Slide 4
Restoration Techniques
Three core capabilities of the system
Noise Removal
› Stage 1: Median Filter (3×3) — removes salt-and-pepper noise
› Stage 2: Non-Local Means Denoising (h=10, window 7×7, search 21×21)
› Patch-based similarity preserves textures & fine details
⏱ ~2.0s
✓ High
Image Deblurring
› Step 1: Horizontal motion blur kernel (5×5)
› Step 2: Wiener Deconvolution in frequency domain via FFT
› Step 3: Unsharp masking (σ=1.0, strength=1.5) sharpens edges
⏱ ~1.0s
✓ Moderate–High
Super Resolution
› Bicubic Interpolation (2× upscale)
› Bilateral Filtering — edge-preserving smooth (d=9)
› Unsharp Masking + Detail Enhancement (σ_s=10, σ_r=0.15)
⏱ ~1.2s
✓ Moderate–High

## Slide 5
DnCNN Deep Learning Model
Residual learning for AI-powered denoising
17-Layer Architecture (PyTorch)
Noisy
Input
Layer 1
Conv + ReLU
Layers 2–16
Conv + BN + ReLU (×15)
Layer 17
Conv Output
Clean
Output
▶
▶
▶
▶
Residual Learning: x_clean = x_noisy − f(x_noisy) → Model predicts NOISE, not the clean image directly
Input Layer
Conv2d(1, 64, 3) + ReLU
1 channel → 64 feature maps
Hidden Layers
Conv2d(64, 64, 3) + BatchNorm2d + ReLU
Repeated ×15 for deep feature extraction
Output Layer
Conv2d(64, 1, 3)
64 feature maps → noise residual
Fallback
If dncnn.pth weights absent, system gracefully falls back to NL-Means classical pipeline

## Slide 6
Implementation Details
Full-stack engineering breakdown
REST API ENDPOINTS
GET
/api/health
Health check
POST
/api/restore
Upload + process
GET
/api/image/:id/input
Original image
GET
/api/image/:id/output
Restored image
FRONTEND FEATURES
Drag & Drop Upload
PNG/JPG/BMP/TIFF/WebP • Max 16 MB
Before/After Slider
CSS clip-path + pointer events for drag comparison
Processing Metrics
Real-time time, method used, and type display
Image Download
One-click export of the restored PNG

## Slide 7
Results & Performance
Benchmarks across all three restoration types
Chart: 
| Noise Removal | Deblurring | Super Resolution
Avg. Processing Time (s) | 2 | 1 | 1.2
Noise Removal
NL-Means + Median
~2.0s
✓ High
Deblurring
Wiener + Unsharp
~1.0s
✓ Mod–High
Super-Res
Enhanced Bicubic
~1.2s
✓ Mod–High
All timings measured on a 400×300 px image. Super resolution output is 2× the input dimensions.

## Slide 8
Conclusion & Future Work
CONCLUSION
✓ Two-stage NL-Means + Median pipeline for effective denoising
✓ Frequency-domain Wiener deconvolution for motion deblurring
✓ Enhanced bicubic 2× super resolution with post-processing
✓ 17-layer DnCNN architecture integrated in PyTorch
✓ Modern React UI with interactive comparison slider
✓ Clean REST API with proper error handling & file management
FUTURE WORK
→ Train DnCNN on BSD68 dataset
→ Integrate ESRGAN / Real-ESRGAN
→ Blind deblurring (auto kernel)
→ Batch processing for multi-image
→ Cloud deploy (AWS / Docker)
→ PSNR + SSIM quality metrics
→ Frame-by-frame video restoration
Thank You!
Questions & Feedback Welcome | Built with React · Flask · OpenCV · PyTorch